Path Planning using Harmonic Potentials

INTRODUCTION

Path planning is the process of creating a set of feasible instructions that guide a robot through its task. Also sometimes called motion planning, the planner produces a set of

The principal types of path planners fall under one of these three umbrellas: exact planners, sampling-based planners, and search-based planners. Artificial Potential Field planners are a subset of exact planners (planners which operate in continuous space).

METHODS

Integral Equation Methods
The integral equations approach calculates the potential field on the boundaries of the domain and its obstacles. From here, ____ theorem can be used to find the potential anywhere within the domain. This is done in by ______ et al. The outer boundary of your environment in addition to the start and goal, can are discretized and the potential is solved for as shown in the elliptic environment below.

A separate integral equation is solved for each of the obstacles in the environment separately. Each of these “obstacle” domains must also include a discretization of the outer boundary of the environment, so that the potential remains between 0 and 1 in both domains. Shown below is one obstacle domain.

When the robot takes a move at each timestep, it is assumed the start and goal and outer boundary positions never change, so the first domain never needs to be recalculated. The obstacle domains however can be recalculated every time they move or new obstacles are discovered in the map.

Algorithm:

According to this algorithm, the robot has a position in both the “base” domain and each “obstacle” domain. Before we move, we must check that the potential at our current position in each obstacle domain. If the potential is less than threshold OMEGA, then we can procede to follow the gradient in the base domain. If however, at any timestep the potential in one of the obstacle domains is greater than OMEGA, we must being “wall-following” or following the contour of the potential field around the obstacle. We take note of the potential, Gin , in the base domain before following the contour. Then, once G < Gin AND the angle between gradG and gradP (P is the potential in the obstacle domain) is less than 90 degrees, we can stop wall-following and continue in the direction of G in the base domain. The first condition is necessary because we dont want to exit the obstacle domain at a higher G than we started at and the second condition is necessary or else we will just be pushed back into the obstacle domain. Under these two conditions, if the robot exits obstacle-following, it will continue toward the goal. If in the event, there is way to the goal, the robot will circle the closest obstacle. After one revolution, we can terminate the algorithm and return that no path exists. In this way it is a complete planner.

Below is a sample path from start to goal with no obstacles. The discretized boundary and normal vectors are drawn.

Finite Elements Method
Finite differences or finite elements can also be used to compute the base domain and obstacle domain.

FURTHER WORK

The algorithm discussed above lets us separate the obstacle domains from the base domain. However, in each obstacle domain, we have discretized the outer boundary to ensure the potential falls to zero there. Without it, the fundamental solution to the Laplace equation, the free space green’s function G = 1/2pi*ln(1/r) falls very quickly as r→ boundary of domain. If, instead, we calculate a new greens function everywhere due to the outer boundary (modelled as a source), we eliminate the need to include the outer boundary in every obstacle domain. This is particularly useful in cases where the environment is known ahead of time, so that the greens function can be calculated offline, and when there are many obstacles moving in the environment.

Finite Elements Method
Show current comparison on FEM analytical and non-analytical
include what constants need to be added so that you can compare solution

Task: Calculate green’s function on 9-point square using analytical solution and using FEM. Compare.

Explanation: To solve
Result:

Integral Equations method
Show square domain integral equation method
Show that you do not have the neumann condition properly defined yet

RESULTS

DISCUSSION

CONCLUSIONS